FK500V Digital Podium

Manual

Please read this manual carefully and keep it well.

# 1,Brief Introduction

The FK 500V multimedia podium adopts an integrated design according to the latest aesthetic theories and international fashion trends; the podium is simply assembled from the upper, middle and lower parts.
This product is a new type of podium that integrates computer technology, touch screen technology, and mechatronics technology. The lecture platform can synchronize video, audio, pictures, text and other information and can automatically adjust the height, and realize related control functions through simple touch control. It is today's world-class multimedia lecture equipment.
It integrates a variety of functions, making the speaker and the host handy, can express the essence of the speaker’s thoughts in all directions, and highlight the elegant style of the host from multiple angles. It is a variety of lecture halls, lecture halls, conference halls, and studios. , Reception rooms, auditoriums, classrooms in large and middle schools, etc., essential and important facilities.

2,Specification

Dimension：765x650x1160mm

FK500V multimedia podium consists of three parts: upper, middle and lower parts;
Integration on the podium:
Gooseneck microphone, LED document light, 21.5-inch touch all-in-one monitor,
control panel
(Contains laptop interface: VGA interface, HDMI interface, USB interface, laptop power socket; LED light switch; gooseneck microphone switch),

Integration of the central column of the podium:
Bottom interface module,

3,Operation manual

1.Connect the 220V power cord to the power socket of the built-in amplifier control panel and turn on the power switch.
2. Turn on the microphone switch on the control panel, the red light on the pickup head of the gooseneck microphone is on, and you can speak normally.
3. Turn on the LED file light switch on the control panel, and the LED light is on.
4. Turn on the electric lift switch of the screen, the display rises, and adjust the display angle of the display.
5. Aluminum wire drawing control panel: HDMI interface, VGA interface, Audio interface, LAN interface and other interfaces are for notebook computers. Connect these interfaces to the corresponding notebook computer output ports and output to external devices from the bottom interface panel.
6. Aluminum wire drawing control panel: USB interface, this interface is the exposed USB interface of the 21.5-inch touch all-in-one monitor, through which the corresponding USB device, such as U disk, can be identified on the touch all-in-one monitor.

4,Bottom Interface Panel

The bottom interface module is mainly to lead the audio and video signals (VGA, HDMI, Audio) of the notebook and touch all-in-one monitor to the bottom of the podium, which is convenient for users to connect to peripheral equipment。

- 21.5” all in one monitor

| Output | HDMI or VGA |
| --- | --- |
| Touch way | 10 point capacitive touch screen |
| Resolution | 720P/1080P |
| Structural design | Aluminum alloy frame, sheet metal back shell, reasonable heat dissipation, optional independently designed base |
| System module | PC、Display and all in one, one key switch |
| Resolution | X86 Ultimate Edition |
| Processor | Intel Conroe i5,4 Generation |
| Operation memory | DDR4 16G |
| Hard disk | 256GSSD |
| Video card | Core Graphics |
| Resolution | 720P/1080P |
| Operating system | Multi touch ：Windows 10 |
| Network card | Integration 10/100/1000M Adaptive network card ，Wireless network adapter 802.11a/b/g/n |
| Input power | 110-240V AC 50/60Hz |